## Slide 1: Note 13 How Computers Work
CSC 2210 Procedural and Object-Oriented C++
Copyright © 2023 Robert W. Hasker

## Slide 2: Basic Structure
This is from note 3
CPU reads instructions from memory
CPU executes the instruction
  Reads data from memory (RAM)
  Use the ALU to compute a result
  Writes result to memory
System bus
  Communicate between RAM, CPU, other devices
  Essentially parallel lines of wires, each wire holding a single bit
  Data, address bus: word width
  Control: a few wires determining read/write, source/destination
How does the CPU work?
Notes: Image from https://en.wikipedia.org/wiki/System_bus

## Slide 3: Logic Gates
Core element: logic gates
Each can be implemented with a small number of transistors, resistors, diodes
Implemented on chip using “doped” bits of silicon
https://instrumentationtools.com/logic-gates/
Notes: Logic gates from https://instrumentationtools.com/logic-gates/

## Slide 4: Logic Gates
Core circuit element
Top to bottom:
  AND
  OR
  NOT
Careful “doping” of silicon can build each
Can also implement each with transistors, resistors, diodes
https://instrumentationtools.com/logic-gates/
Notes: Images from https://instrumentationtools.com/logic-gates/

## Slide 5: 1-bit full adder
A, B: input bits
Cin: carry from previous addition
S: result
Cout: Carry out
String multiples together for a full adder
Notes: Try cases: A = 0, B = 1, Cin = 1; etc
Diagram available many places, but this one from https://www.build-electronic-circuits.com/4000-series-integrated-circuits/ic-4008/

## Slide 6: Using the full adder
Notes: From same site as previous

## Slide 7: Multiplexor Circuit
Add: ALU
Key issue in CPU: how to route data
Solution: MUX (multiplexor)
  Select from alternative inputs
And gate with circle: NAND
  Convenient shorthand
a, b: select between A/B/C/D
This scales to any power of 2
Mirror image: 1 to many
  Demultiplexor (DEMUX)
Data Inputs
Select
Switch Analogy
(4 positions)
NAND
gates
Truth table
Notes: Image from https://www.electronics-tutorials.ws/combination/comb_2.html
See https://en.wikipedia.org/wiki/Multiplexer for additional discussion

## Slide 8: Constructing a processor
Elements
  Circuits to store data
    For registers, these are typically feedback circuits that refresh on each cycle
  ALU: essentially add/subtract with loops for multiplication
    Optimized to reduce gate delay between input and output
  Selectors: route data in CPU as required by instruction
  Additional element: clock line so circuits can “settle” to get predictable output
Selectors controlled by instruction decoder
  This can be a table of settings for each instruction
  It can even be programmable: “microcode”

## Slide 9: 8086 Layout
Note registers, adder
Control: generally MUX/DEMUX circuits
  Also contains clock
ALU: logic circuits
Flags: neg, overflow, etc.
Microcode: decode instructions to set MUX/DEMUX circuits

## Slide 10: Review
Basic gates: AND/OR/NOT
  Also have NAND, NOR
  Interesting result: can create other gates from NAND, NOR
  Theoretical result: all computers can be built from a single type of gate!
MUX: select between different inputs
  DEMUX: chose output
Microcode: control selectors for instructions
Processor design as registers + ALU + control + instruction decoder
Question: how is this relevant to programmers?

## Slide 11: Computing Abstractions
Starting point: programming in a high level language
  Java, Python, C++
  Lots of abstractions to support overall system design
  Mathematical, ADT views of types
This course: introduction to low level programming: C
  Programmer must know internal details
  Often focused on types=string of bits
  Abstractions must be maintained by the programmer
Also in this course: assembly programming
  In our case, using the x86 architecture

## Slide 12: Computing Abstractions
Mathematics: proving code is correct
High level languages: Java, C++, Python
Low level languages: C, Fortran
Assembly programming
Microcode: programming processors (or equivalent to microcode)
Gate logic: AND, OR, NOT
High/low voltage circuits: 0-.7 volts represent 0, 1.5-5 volts represent 1 (say)
Transistors/resistors/diodes: implementing the circuits
Quantum mechanics: implementing transistors/other elements in silicon
Mathematics: understanding quantum mechanics
Practical outcome of this course:
Being able to think at each level
Programmers can stick to 1-4
Awareness of 5-8 useful
9: might be relevant to quantum computing!
Notes: Few processors use microcode today, favoring hard-wired circuits, but need something to go from instructions to selecting circuits and timing