## Slide 1: Pulse-Width Modulation
SWE4211

## Slide 2: Outcomes
Explain the concept of PWM.
Explain how PWM can be used to control a motor.
From a waveform, calculate the duty-cycle for a PWM signal.
Measure the PWM duty cycle with an oscilloscope.
Compare and Contrast software and hardware driven PWM.

## Slide 3: Today’s thought of the day…

## Slide 4: Lab Study
What did we see in our lab 3 assignments?

## Slide 5: Blinking Light

## Slide 6: What is wrong with this graph?
What number goes with what line?
Do we need to see these numbers to the nearest tenth?
Can users see the difference between 2000 Hz and 8000 Hz?
  Critical data is 0-60 Hz, maybe up to 200 Hz
  Use log scale!
How can the Python minimum be zero?

## Slide 7: What is wrong with this graph?
Graph should show period, not frequency
Graph goes down rather than up

## Slide 8: What is wrong with this graph?
What type of blink rate on the bottom?
What is going on at 1000 Hz?
  These sorts of jumps are unlikely to be physical – suggest incorrect data collection or analysis

## Slide 9: What is wrong with this graph?

## Slide 10: Error Plots
Chart: Blinking LED Percent Error Plot
| 1 | 5 | 10 | 50 | 100 | 500 | 1000 | 5000 | 10000
Regular Python Error | 0.02 | 0.08 | 0.161 | 0.47908 | 0.646 | 0.9008 | 0.9486 | 0.98928 | 0.9946
Performance Python Error | 0.0095 | 0.04528 | 0.08664 | 0.32228 | 0.487 | 0.82585 | 0.90507 | 0.97951 | 0.98964
Regular C++ Error | 0.0001 | 0.006 | 0.0003 | 4e-05 | 0.00422 | 0.019882 | 0.039 | 0.16324 | 0.28991
Performance C++ Error | 2e-05 | 8e-05 | 0.0016 | 0.00086 | 0.00185 | 0.0088 | 0.0173 | 0.07994 | 0.15842
Regular Rust Error | 0.00021 | 0.00082 | 0.0002 | 0.0079 | 0.01595 | 0.0748 | 0.13278 | 0.43914 | 0.61032
Performance Rust Error | 0.00014 | 6.4e-05 | 0.00128 | 0.00626 | 0.00216 | 0.0593 | 0.11125 | 0.38306 | 0.55421

## Slide 11: Latency Plots
Delay (ms) | Python 1 | Python 2 | Python 3 | C++1 | C++2 | C++3 | Rust 1 | Rust 2 | Rust 3 | Delay2 | Python Max | C++ Max | Rust Max | Python Median (ms) | C++ Median (ms) | Rust Median (ms)
0 | 4.7 | 0 | 4.8 | 0.0003 | 0.0005 | 0.0004 | 0.0001 | 0.0001 | 0.0002 | 0.1 | 4.8 | 0.0005 | 0.0002 | 4.7 | 0.0004 | 0.0001
10 | 17 | 24 | 8.5 | 5 | 1 | 4 | 0.5 | 3.2 | 7.2 | 10 | 24 | 5 | 7.2 | 17 | 4 | 3.2
100 | 90 | 30 | 80 | 45 | 52 | 45 | 98 | 46 | 56 | 100 | 90 | 52 | 98 | 80 | 45 | 56
1000 | 640 | 260 | 900 | 510 | 500 | 610 | 420 | 260 | 840 | 1000 | 900 | 610 | 840 | 640 | 510 | 420
Units?

## Slide 12: What is different?

## Slide 14
How it works:
DC Motors
When reach halfway point, electromagnet switches
Result is spin
  May have 3 (or more?) magnets
  Uses brushes: wear
AC motor: ring of sequenced magnets
How can the Pi drive a motor?
GPIO Pins: direct current
Adding an alternator wastes power
Maybe we could simulate an AC wave...
Notes: Image from https://www.caretxdigital.com/electric-stove-connection-diagram/

## Slide 15: PWM
Goal, emulate a sine wave using a DC output pin
Don’t need the curve, just the change in direction
Solution: pulse-width modulation (PWM)
Essentially, fake it!
Also used for dimmers, sound, etc.
Notes: sine wave Graphic from https://www.desmos.com/calculator/w9jrdpvsmk
PWM material at https://www.wevolver.com/article/what-is-a-pwm-signal-fundamentals-and-practical-applications-for-engineers among other places
PWM graphic from this page

## Slide 16: Contemplation
How does one control the speed of a motor?
How does one change the brightness of a light bulb?

## Slide 17: PWM Personified

## Slide 18: Effective Voltage provided by PWM
Determine the duty cycle (D): “tau over tee”
  Fraction of period where signal is high
  tau: time on, T: time period
Compute the effective voltage (Veff):
  Multiply the duty cycle by the peak voltage
  Vp: peak voltage – how high the signal goes

## Slide 19: Calculating the Effective Voltage with PWM
Example
Tau = .1 s
T = 1 second
Duty cycle = 10%
If vP = 5 volts, effective voltage is .5 V
Tau = .25 s
T = .75s
Duty cycle = 33%
If vP=5 volts, effective voltage = 1.65 v
High voltage on this graph: 5 V
= ¼
Veff = 1.25
Notes: Example
Tau = .1 s
T = 1 second
Duty cycle = 10%
If vP = 5 volts, effective voltage is .5 V
Tau = .25 s
T = .75s
Duty cycle = 33%
If vP=5 volts, effective voltage = 1.65 v

## Slide 20: PWM Measurement
Let's look at some PWM with the Raspberry PI and an LED.

## Slide 21: Hardware versus software PWM
How would hardware PWM works?
  Typically: PLC
Software PWM – what do you think are the advantages?
What are the advantages of hardware?

## Slide 22: Lets look at the code for the project we just ran

## Slide 23: Discussion
What happens to CPU utilization as the period of the PWM signal changes?
What happens to CPU utilization as the duty cycle of the PWM signal changes?
What happens if the PWM signal period gets too long?
What does the oscilloscope show as we change period, duty cycle?

## Slide 24: Hardware Versus Software PWM