## Slide 1: Division
Perform binary division of two numbers.
Define dividend, divisor, quotient, and remainder.
Explain how division is accomplished in computer hardware.
Construct a simple program which uses MIPS integer multiplication and division

## Slide 2: Definitions (Pg 237)
Dividend
  The first operand of a divide operation
Divisor
  The second operand of a divide operation
Quotient
  The primary result of a divide operation
Remainder
  The secondary result of a division operation
14 / 5 = 2 rem 4

## Slide 3: Division (Long Approach)
Solve the following

## Slide 4: Division Algorithm
Check for 0 divisor first!
Long division approach
  If divisor ≤ dividend bits
    1 bit in quotient, subtract
  Otherwise
    0 bit in quotient, bring down next dividend bit
Restoring division
  Do the subtract, and if remainder goes < 0, add divisor back
Signed division
  Divide using absolute values
  Adjust sign of quotient and remainder as required

## Slide 5: Faster Division
Can’t use parallel hardware as in multiplier
  In multiplication, we can compute partial products simultaneously
  In division, we have to compute differences at each step
Faster dividers (e.g. SRT division) generate multiple quotient bits per step
  Still require multiple steps, using guesses and corrections
  Uses a lookup table that must be precomputed
    Source of infamous 1994 Pentium flaw

## Slide 6: MIPS Division
Use HI/LO registers for result
  HI: 32-bit remainder
  LO: 32-bit quotient
Instructions
  div rs, rt / divu rs, rt
  No overflow or divide-by-0 checking!
    Software must perform checks if required
  Use mfhi, mflo to access result
    $hi and $lo are left unchanged during divide-by-0!
    They contain whatever values they had prior to divide-by-0

## Slide 7: In Class Example
Write an assembly program which will perform the following:
  Read two integer numbers from the user
  Print out their product
  Print out their quotient
  Print out the remainder (If the numbers are not evenly divisible)