## Slide 1: CS2911 Week 1, Class 1
Today
  Introductions
  Syllabus and Class/Lab Layout
  Safety Review - Note about Lab Safety Review
  Networking a Game
  Network Layers and Packet Headers
  Lab 2 starts today!
  Binary encodings
  Muddiest Point
Notes: print 1,12,13,16-19,22-26

## Slide 2: Introductions
Find someone you don’t know and learn
  Their name
  One interesting thing they did this summer
Be prepared to tell this to the rest of the class
Just 2 minutes… make sure you all get a turn!

## Slide 3: Syllabus and Class Layout
See http://faculty-web.msoe.edu/yoder/cs2911

## Slide 4: Safety Review
Take notes

## Slide 5: Networking Sand Blaster
See handout

## Slide 6: Network Layers
Internet protocol stack
Physical
Link
Network
Transport
Application

## Slide 7: Nested Packets
Ethernet Packet

## Slide 8: Nested Packets
Ethernet
Header
Ethernet Payload

## Slide 9: Nested Packets
Ethernet
Header
IP
Header
IP Payload

## Slide 10: Nested Packets
Ethernet
Header
IP
Header
TCP
Header
TCP Payload

## Slide 11: Nested Packets
Ethernet
Header
IP
Header
TCP
Header
HTTP
Header
HTTP
Payload

## Slide 12: Nested Packets
Ethernet
Header
Ethernet Payload
Ethernet
Header
IP
Header
IP Payload
Ethernet
Header
IP
Header
TCP
Header
TCP Payload
Ethernet
Header
IP
Header
TCP
Header
HTTP
Header
HTTP
Payload

## Slide 13: Binary Encodings
You can store anything as 1's and 0's
Exercise: Brainstorm the types of things that you might want to send over the internet

## Slide 14: How do we send these things over the internet?
You may need a few sheets of paper to hold your notes on this
First page may be best in landscape

## Slide 16
Binary | Hexadecimal
0000 | 0
0001 | 1
0010 | 2
0011 | 3
0100 | 4
0101 | 5
0110 | 6
0111 | 7
Binary | Hexadecimal
1000 | 8
1001 | 9
1010 | A
1011 | B
1100 | C
1101 | D
1110 | E
1111 | F

## Slide 17: What's a byte?
A byte is 8 bits.
So 100010 can be written with two bytes:
0000 0011 1110 1000
How do you write this in hexadecimal?

## Slide 18: Representing characters with bytes
ASCII characters:
0100 0001 ‘A’
0100 0010 ‘B’
0110 0001 ‘a’
0011 0000 ‘0’
0011 0001 ‘1’
0000 1101 ‘\r’ CR (Carriage return)
0000 1010 ‘\n’ LF (Line feed, New line)
0010 0000 ‘ ’ (Space)
0100 0001
‘A’
Byte
nibble
code
character
Notes: (17q1: edited after class)

## Slide 19
Exercise: How to represent ASCII ‘A’, CR, and LF in hexadecimal?
Exercise: How do you write the ASCII string "Cab" in hexadecimal bytes?

## Slide 20: You are now ready to finish Lab 2!
Overview Lab 2 – see website

## Slide 21
Notes: What was the muddiest point?
Poll Title: What was the muddiest point? (CS2910) https://www.polleverywhere.com/free_text_polls/zIp2tH2IVWjXv4H

## Slide 22: Exercise
Exercise: What does the byte 0x44 mean if interpreted as an ASCII character?
Exercise: What does the byte 0x44 mean if interpreted as a binary number?

## Slide 23
Binary | Octal
000 | 0
001 | 1
010 | 2
011 | 3
100 | 4
101 | 5
110 | 6
111 | 7
Binary | Octal
unused | 8
unused | 9

## Slide 24: Big endian / little endian
100010 can be written with the bytes
big endian: most significant byte first
0000 0011 1110 1000
little endian: least significant byte first
1110 1000 0000 0011
Ex: What do these look like in hexadecimal?
Network order is BIG ENDIAN (whew!)
Intel machines are LITTLE ENDIAN

## Slide 25
Exercise 1: How many values can you represent with 1 bit? 2? 3? 4? 5? 6? 7? 8? 9? 10? n bits?
Exercise 2: How many bits can you represent with a single decimal digit (0-9)?

## Slide 26: Acknowledgement
This course is based on the text
Computer Networking: A Top Down Approach 7th edition Jim Kurose, Keith Ross Addison-Wesley
Notes: Book image added later