## Slide 1: CS2911 Week 7, Class 3
Today
  Muddiest Point
  Questions on Videos
  Finish TCP
  Encryption
  Muddiest Point
Week 8, Lab period
  Quiz 4: Topics include TCP, SMTP, IMAP, POP
Notes: 17q1 7-1 1-7,9-24

## Slide 2: Sliding Window supports Flow Control
Won't over-fill receiver's buffer
Waits for receiving application to be ready
This is one reason to call recv even before we have gotten the whole message

## Slide 3: Flow vs. Congestion Control
Flow control is a function of the receiver and its ability to accept data
Congestion control is a function of the network and its ability to carry messages
Congestion control avoids sending more data than the network can handle, resulting in collapse of the network

## Slide 4: New Variable - cwnd
Two windows
    Un-acknowledged bytes
  cwnd – congestion window
  rwnd – receive (flow control) window
Notes: Note that this is NOT a new field in the headers – convenient!

## Slide 5: cwnd
We can send up to cwnd bytes per RTT period
Average transmission rate is roughly cwnd/RTT bytes/sec
By manipulating cwnd, transmission rate can be controlled

## Slide 6: Congestion Detection
If segments lost, maybe we are sending too many
Adjust cwnd
  Decrease when a segment is lost
  Increase when [consistent] ACKs are received
    Continue to increase until a segment is lost, then backoff

## Slide 7: TCP Slow Start
Start with a small cwnd (one MSS)

## Slide 8: cwnd Over Time

## Slide 9: Challenge: How to avoid accidental message?
What if a TCP message from a previous connection gets stuck in a router for a while, but then eventually gets delivered later?
How to avoid it being mistaken for the newer message?

## Slide 10: A very brief history of the internet
1957 – Sputnik launched, ARPA formed
1962 – ARPA forms IPTO to create ARPAnet
1969 – First packet switched network at UCLA
1971 – First emails with @ signs
1983 – TCP/IP first deployed
1986 – NSFNET created (& many others)
1989 – HTTP starts with just GET
1991 – NSFNET allows commercial activities. e-Bay, Google, Amazon …
2000's – Facebook, Twitter, Youtube, …
Source: Kurose & Ross, 6th, Ed, Section 1.7 and
http://www.calvin.edu/academic/rit/webBook/chapter3/Introduction/arpanet.htm
http://www.livinginternet.com/e/ei.htm Wiki: HTTP

## Slide 11: Questions about Encryption
What are the different ways in which a message can be damaged? How can someone eavesdrop over the network? | Big picture: Intrusion techniques
What are some everyday things that use encryption, like things that we wouldn't necessarily think about? | Big picture: What uses encryption?
1. I still feel confused about the concept of the key. Is the key a number? Or it is a function for encoding the plaintext? | Big picture: What is a key?
2. What is the known plaintext attack? | 

## Slide 12: Questions about Encryption
If someone found a way to determine the encryption algorithm, would they be able to then create a decryption algorithm? The video says that they could introduce false information into the cipher-text, but I would assume a more valuable use would be to reverse engineer it to decode the cipher-text. For the box algorithm, it says that it uses a table that grows in size 2^n where n is the number of bits in each chunk. Couldn't the size of the chunk just be kept small? And why does it require a table that grows at such a fast rate? | Big picture: What is a key?

## Slide 13: Questions about Encryption
if encryption algorithms are often in the public domain, wouldn't cipher block chaining become recognizable to an intruder studying the cipher text? | Cipher block chaining
when talking about keys, is it possible to have a public and private key that is known to encrypt a private key for even greater security of information, or is public private key only used for sending / receiving messages? | Public/private keys
What are some common encryption algorithms that use the methods in the video, like symmetric? | Current Algorithms

## Slide 14: Questions about Encryption
Is there ever a good use for simple symmetric cyphers? It seems easy to guess through brute force, so why would anybody use such a weak encryption? | Why use simple encryption?
So I remember hearing somewhere that Prime numbers are really important when it comes to encryption. How would that apply to Stream, Block, and Cipher Block Chaining encryption strategies? | Prime numbers

## Slide 15: Questions about Encryption
How are the keys (Ka and Kb) sent? Wouldn't they need to be encrypted with a second set of keys, and then those keys would need to be encrypted by a different set of keys, ad infinitum? Or do the keys exist somehow on the sending and receiving machines independent of the network? | Public/private keys
How are asymmetric keys used to encrypt the text? It doesn't seem inherently true that the order in which the keys are used on the text doesn't matter. | Public/private keys
Is it possible for a company to have multiple was of encoding? That way they can alternate and it will be really hard for Trudy to get near deciphering the encryption. | Encryption strategy

## Slide 16: Questions about Encryption
What is the point of a basic Casesar cypher? It is far too easy to decrypt to actually be used for private information. | Why use simple encryption?
How exactly are keys used? I understand the concept, but how are the client and host made aware of the same key to use, despite the fact that sending the key over the network would require encryption for obvious reasons? | Sharing keys
How come the person receiving the message can decipher the message but an intruder can't? How does the receiver get the key but not the intruder? | Sharing keys
What is the purpose of a session key? How does is differ from the public and private keys? | Symmetric vs. Asymmetric

## Slide 17: Questions about Encryption
Does encryption always use a symmetric key system? If not, how would a non-symmetric key system work when encrypting and decrypting plain text? | public/private keys
Is this some of the fundamentals of learning how to become a hacker? How and where can you find the keys or figure out which type of encryption system is being used? | Cracking keys and algorithms
what is the current standard for encryption? | Current algoritms

## Slide 18: Questions about Encryption
During stream ciphers, he mentioned encoding by adding another stream of bytes, (e sub i in the video). Is this a generated stream, or are you trying to interlace two streams of actual data? When you decode, are you trying to find both b sub i(plaintext bytestream) and e sub i? or just b sub i? [See Chapter 8.8.1, 7th Ed.] | Stream ciphers
are session keys shared secret keys? | Symmetric keys
how are "secret" keys shared but kept secret? | Sharing keys
 | Known plaintext attack

## Slide 19: Questions about Encryption
For session keys, wouldn't there be a finite amount of keys that could be generated before the computation would become too taxing on the computer system and therefore would be more reasonable to cycle back to older keys? | Computation-al burden, Repeated keys
The session key is generated as a new one every time. Is there any chance that after times there will be repeated key? | Repeated keys
What other types of encryption are there besides rsa | Current Algorithms

## Slide 20: Comments about Encryption
Why can't we all just promise not to intrude on others, so this becomes unnecessary? hahaha. | 
Are we going to have to encrypt? | 
These videos are a bit slow-paced, but playing at 1.5 speed mitigates this. YouTube is great! | 
Are there common keys and encryption standards for cryptography? | 
I like the section which introduces the relationship between the plain text and the cipher text. The graph is helpful for me to understand the relationship. | 
If the keys are suppose to come in and out of existence, how is someone potentially able to trackback to previous transactions? | 

## Slide 21
Notes: Poll Title: What was the muddiest point? (CS2911) https://www.polleverywhere.com/free_text_polls/zIp2tH2IVWjXv4H

## Slide 22: Acknowledgement
The content of this video is based in part on lecture slides from a very good textbook, and used with the author’s permission:
Computer Networking: A Top-Down Approach, 7th edition, by Jim Kurose and Keith Ross
Publisher: Pearson, 2017
It is also based on slides provided by Dr. Darrin Rothe