## Slide 1: CS2911 Week 1, Class 1
Today
  Introductions
  Syllabus
  Safety Review
  Lab 2 starts at our next meeting!
  Binary encodings
  Muddiest Point
Notes: print 1,12,13,16-19,22-26

## Slide 2: Introductions
Find someone you don’t know and learn
  Their name
  One interesting thing they did this summer
Be prepared to tell this to the rest of the class
Just 2 minutes… make sure you all get a turn!

## Slide 3: Syllabus and Class Layout
See http://faculty-web.msoe.edu/yoder/cs2911
    Instructional Vocabulary for ESL students

## Slide 4: Safety Review
Take notes

## Slide 5: Binary Encodings
You can store anything as 1's and 0's
Exercise: Brainstorm the types of things that you might want to send over the internet

## Slide 6: How do we send these things over the internet?
You may need a few sheets of paper to hold your notes on this
First page may be best in landscape

## Slide 8: What's a byte?
A byte is 8 bits.
So 100010 can be written with two bytes:
0000 0011 1110 1000
How do you write this in hexadecimal?

## Slide 9: Representing characters with bytes
ASCII characters:
0100 0001 ‘A’
0100 0010 ‘B’
0110 0001 ‘a’
0011 0000 ‘0’
0011 0001 ‘1’
0000 1101 ‘\r’ CR (Carriage return)
0000 1010 ‘\n’ LF (Line feed, New line)
0010 0000 ‘ ’ (Space)
0100 0001
‘A’
Byte
nibble

## Slide 10: Required ASCII characters
Hex code | Char |  | Hex code | Char |  | Hex code | Char |  | Hex code | Char
0d | '\r' CR |  | 30 | '0' |  | 41 | 'A' |  | 61 | 'a'
 |  |  | 31 | '1' |  | 42 | 'B' |  | 62 | 'b'
0a | '\n' LF |  | … | … |  | 43 | 'C' |  | 63 | 'c'
 |  |  | 38 | '8' |  | 44 | 'D' |  | 64 | 'd'
20 | ' ' SP |  | 39 | '9' |  | 45 | 'E' |  | 65 | 'e'
Notes: 17q1 added after class, "Hex code" added day of Lab 3

## Slide 11
Exercise: How to represent ASCII ‘A’, CR, and LF in hexadecimal shorthand?
Exercise: How do you write the ASCII string "Cab" in hexadecimal shorthand?

## Slide 12: UDP Header
 | Byte | 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
Byte | Bit | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
0 | 0 | Source port |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Destination port |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4 | 32 | Length |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Checksum |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Wikipedia: User Datagram Protocol

## Slide 13: You are now ready to finish Lab 2!
Overview Lab 2 – see website

## Slide 14: Questions about Lab 2?
What we've discussed today
Python code in lab assignment
Role of UDP in network stack
…

## Slide 15: Symbols

## Slide 16: Exercise: Complete the hexadecimal column
Binary | Hexadecimal
0000 | 0
0001 | 1
0010 | 2
0011 | 
0100 | 
0101 | 
0110 | 
0111 | 
Binary | Hexadecimal
1000 | 
1001 | 
1010 | 
1011 | 
1100 | 
1101 | 
1110 | 
1111 | f

## Slide 17
Binary | Octal
000 | 0
001 | 1
010 | 2
011 | 3
100 | 4
101 | 5
110 | 6
111 | 7
Binary | Octal | Decimal
1000 | 10 | 8
1001 | 11 | 9
1010 | 12 | 10
1011 | 13 | 11
1100 | 14 | 12
1101 | 15 | 13
1110 | 16 | 14
1111 | 17 | 15

## Slide 18: What's a byte?
A byte is 8 bits.
Exercise: Consider the hexadecimal byte-dump
e8 02 1a ff
Circle the first byte in this dump
Write this byte in binary

## Slide 19: Exercise
Exercise: What does the byte 0x62 mean if interpreted as an ASCII character?
Exercise: What does the byte 0x62 mean if interpreted as a binary number?

## Slide 20: Exercise
Exercise: What does the byte 0x44 mean if interpreted as an ASCII character?
Exercise: What does the byte 0x44 mean if interpreted as a binary number?

## Slide 21: Big endian / little endian
100010 can be written with the bytes
big endian: most significant byte first
0000 0011 1110 1000 (03 e8)
little endian: least significant byte first
1110 1000 0000 0011 (e8 03)
Network order is BIG ENDIAN (whew!)
Intel machines are LITTLE ENDIAN

## Slide 22: Exercise
Convert the number 700 to binary
Write 700 in big-endian format (in binary)
Convert the binary to hexadecimal shorthand
Write 700 in little-endian (hexadecimal shorthand)
Repeat for 443, 587 (these are ports we will use later in the quarter)

## Slide 23
Exercise 1: How many values can you represent with 1 bit? 2? 3? 4? 5? 6? 7? 8? 9? 10? n bits?
Exercise 2: How many bits can you represent with a single decimal digit (0-9)?

## Slide 24
Notes: Poll Title: What was the muddiest point? https://www.polleverywhere.com/free_text_polls/zIp2tH2IVWjXv4H

## Slide 25: Exercise
Exercise: What does the byte 0x44 mean if interpreted as an ASCII character?
Exercise: What does the byte 0x44 mean if interpreted as a binary number?

## Slide 26
Binary | Octal
000 | 0
001 | 1
010 | 2
011 | 3
100 | 4
101 | 5
110 | 6
111 | 7
Binary | Octal
unused | 8
unused | 9

## Slide 27: Big endian / little endian
100010 can be written with the bytes
big endian: most significant byte first
0000 0011 1110 1000
little endian: least significant byte first
1110 1000 0000 0011
Ex: What do these look like in hexadecimal?
Network order is BIG ENDIAN (whew!)
Intel machines are LITTLE ENDIAN

## Slide 28
Exercise 1: How many values can you represent with 1 bit? 2? 3? 4? 5? 6? 7? 8? 9? 10? n bits?
Exercise 2: How many bits can you represent with a single decimal digit (0-9)?

## Slide 29: Wireshark Demo
See Wireshark

## Slide 30: Acknowledgement
This course is based on the text
Computer Networking: A Top Down Approach 7th edition Jim Kurose, Keith Ross Addison-Wesley
Notes: Book image added later