## Slide 1: CS2911 Week 1, Lab
Today
  Safety Review
  Binary encodings
  Muddiest Point
  Lab 1 starts!
Wednesday
  Introductions
  Syllabus
Notes: print 1,12,13,16-19,22-26

## Slide 2: Safety Review
Take notes

## Slide 3: Binary Encodings
You can store anything as 1's and 0's
Exercise: Brainstorm the types of things that you might want to send over the internet

## Slide 4: How do we send these things over the internet?
You may need a few sheets of paper to hold your notes on this
First page may be best in landscape

## Slide 6: What's a byte?
A byte is 8 bits.
So 100010 can be written with two bytes:
0000 0011 1110 1000
How do you write this in hexadecimal?

## Slide 7: Representing characters with bytes
ASCII characters:
0100 0001 ‘A’
0100 0010 ‘B’
0110 0001 ‘a’
0011 0000 ‘0’
0011 0001 ‘1’
0000 1101 ‘\r’ CR (Carriage return)
0000 1010 ‘\n’ LF (Line feed, New line)
0010 0000 ‘ ’ (Space)
0100 0001
‘A’
Byte
nibble

## Slide 8: Required ASCII characters
Hex code | Char |  | Hex code | Char |  | Hex code | Char |  | Hex code | Char
0d | '\r' CR |  | 30 | '0' |  | 41 | 'A' |  | 61 | 'a'
 |  |  | 31 | '1' |  | 42 | 'B' |  | 62 | 'b'
0a | '\n' LF |  | … | … |  | 43 | 'C' |  | 63 | 'c'
 |  |  | 38 | '8' |  | 44 | 'D' |  | 64 | 'd'
20 | ' ' SP |  | 39 | '9' |  | 45 | 'E' |  | 65 | 'e'
Notes: 17q1 added after class, "Hex code" added day of Lab 3

## Slide 9
Exercise: Suppose the ASCII characters ‘A’, CR, and LF are stored in a bytes object. Write the hexadecimal shorthand for the contents of the bytes object.
Exercise: How do you write the ASCII string "Cab" in hexadecimal shorthand?

## Slide 10: UDP Header
 | Byte | 0 |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  | 
Byte | Bit | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
0 | 0 | Source port |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Destination port |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4 | 32 | Length |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Checksum |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Wikipedia: User Datagram Protocol

## Slide 11: You are now ready to finish Lab 2!
Overview Lab 2 – see website

## Slide 12: Questions about Lab 2?
What we've discussed today
Python code in lab assignment
Role of UDP in network stack
…

## Slide 13: CS2911 Week 1, Class 1
Today
  Syllabus
  Introductions
Lab
  Safety Review
  Binary encodings
  Lab 1 starts!
Notes: print 1,12,13,16-19,22-26

## Slide 14: Syllabus and Class Layout
http://faculty-web.msoe.edu/yoder/cs2911
    Syllabus
    Free resources for students
    Lab schedule
    Teams of two
    Python Coding Standard
    Instructional Vocabulary for ESL students

## Slide 15: Mental Health
More than 25% of college students have been diagnosed or treated by a professional for a mental health condition within the past year
Suicide is the 3rd leading cause of death on college campuses.
64% of young adults who are no longer in college are not attending college because of a MH related reason.
Notes: Source: MSOE’s wellness center.

## Slide 16: Introductions
Find someone you don’t know and learn
  Their name
  One interesting thing they did this summer
Be prepared to tell this to the rest of the class
Just 2 minutes… make sure you all get a turn!

## Slide 17: Questions?

## Slide 18: Symbols

## Slide 19: Exercise: Complete the hexadecimal column
Binary | Hexadecimal
0000 | 0
0001 | 1
0010 | 2
0011 | 
0100 | 
0101 | 
0110 | 
0111 | 
Binary | Hexadecimal
1000 | 
1001 | 
1010 | 
1011 | 
1100 | 
1101 | 
1110 | 
1111 | f

## Slide 20
Binary | Octal
000 | 0
001 | 1
010 | 2
011 | 3
100 | 4
101 | 5
110 | 6
111 | 7
Binary | Octal | Decimal
1000 | 10 | 8
1001 | 11 | 9
1010 | 12 | 10
1011 | 13 | 11
1100 | 14 | 12
1101 | 15 | 13
1110 | 16 | 14
1111 | 17 | 15

## Slide 21: What's a byte?
A byte is 8 bits.
Exercise: Consider the hexadecimal byte-dump
e8 02 1a ff
Circle the first byte in this dump
Write this byte in binary

## Slide 22: Exercise
Exercise: What does the byte 0x62 mean if interpreted as an ASCII character?
Exercise: What does the byte 0x62 mean if interpreted as a binary number?

## Slide 23: Exercise
Exercise: What does the byte 0x44 mean if interpreted as an ASCII character?
Exercise: What does the byte 0x44 mean if interpreted as a binary number?

## Slide 24: Big endian / little endian
100010 can be written with the bytes
big endian: most significant byte first
0000 0011 1110 1000 (03 e8)
little endian: least significant byte first
1110 1000 0000 0011 (e8 03)
Network order is BIG ENDIAN (whew!)
Intel machines are LITTLE ENDIAN

## Slide 25: Exercise
Convert the number 700 to binary
Write 700 in big-endian format (in binary)
Convert the binary to hexadecimal shorthand
Write 700 in little-endian (hexadecimal shorthand)
Repeat for 443, 587 (these are ports we will use later in the quarter)

## Slide 26
Exercise 1: How many values can you represent with 1 bit? 2? 3? 4? 5? 6? 7? 8? 9? 10? n bits?
Exercise 2: How many bits can you represent with a single decimal digit (0-9)?

## Slide 27
Notes: Poll Title: What was the muddiest point? https://www.polleverywhere.com/free_text_polls/zIp2tH2IVWjXv4H

## Slide 28: Exercise
Exercise: What does the byte 0x44 mean if interpreted as an ASCII character?
Exercise: What does the byte 0x44 mean if interpreted as a binary number?

## Slide 29
Binary | Octal
000 | 0
001 | 1
010 | 2
011 | 3
100 | 4
101 | 5
110 | 6
111 | 7
Binary | Octal
unused | 8
unused | 9

## Slide 30: Big endian / little endian
100010 can be written with the bytes
big endian: most significant byte first
0000 0011 1110 1000
little endian: least significant byte first
1110 1000 0000 0011
Ex: What do these look like in hexadecimal?
Network order is BIG ENDIAN (whew!)
Intel machines are LITTLE ENDIAN

## Slide 31
Exercise 1: How many values can you represent with 1 bit? 2? 3? 4? 5? 6? 7? 8? 9? 10? n bits?
Exercise 2: How many bits can you represent with a single decimal digit (0-9)?

## Slide 32: Wireshark Demo
See Wireshark

## Slide 33: Acknowledgement
This course is based on the text
Computer Networking: A Top Down Approach 7th edition Jim Kurose, Keith Ross Addison-Wesley
Notes: Book image added later