## Slide 1: CS-498 Computer Vision
Week 7, Day 2
  Camera Parameters
    Intrinsic Calibration
      Linear
      Radial Distortion
    (Extrinsic Calibration?)
Notes: Print

## Slide 2
Optic center
Optic axis intersects unit plane perpendicularly
x
y
z

## Slide 3: Linear Pinhole Camera
(linear in homogeneous coordinates)
Projection model:
Light projects along straight line onto unit plane
To find the pixel index in each dimension,
multiply by pixels/unit (focal length)
add the index of the optic center

## Slide 4: Intrinsic Calibration
The Intrinsic Parameters describe the part of the calibration that does not change if you move or rotate the camera
“Unit” camera:

## Slide 5: “Full” camera
fi = focal length in the i direction (pixels per unit distance along unit plane in the i direction)
fj = focal length in the j direction (pixels per unit distance along unit plane in the j direction)
ci = center of the image, measured in pixels
cj = center of the image, measured in pixels

## Slide 6: Exercise
Using the information on the previous slides,
Suppose a camera has the following parameters:
Both focal lengths – 100 pixels/unit
Center – 50 pixels down, 75 pixels to the right
Find:
1. The i,j coordinates of the point (0,0,10)
2. The i,j coordinates of the point (0,10,10)

## Slide 7: Lab Exercise
Given i, j, and z… find x and y

## Slide 8: Radial Distortion
If we took a picture of concentric circles…
It might come out like…
This is radial distortion

## Slide 9: Radial Distortion Pinhole Camera
Projection model:
Light projects along straight line onto unit plane
Within unit plane, account for radial distortion
To find the pixel index in each dimension,
multiply by pixels/unit (focal length)
add the index of the optic center

## Slide 10: Equations for radial distotion
xnew = xold (1+cx1xold2+cx2xold4+…)
ynew = yold (1+cy1yold2+cy2yold4+…)

## Slide 11: Extrinsics Parameters
What changes as the camera moves
Translation – position of optic center
  [x,y,z] – 3 numbers
Rotation – Multiplication of three rotation matrices, around each axis
  Roll, pitch, yaw – 3 numbers
  Matrix has 9 numbers, but these can
  be found from just 3, and will always have values
  between -1 and 1; very constrained.

## Slide 12
[Insert full transform here]