## Slide 1: CS-498 Computer Vision
Week 7, Day 2
  Camera Parameters
    Intrinsic Calibration
      Linear
        Forward and backward projection
Notes: Print

## Slide 2
Optic center
Optic axis intersects unit plane perpendicularly
x
y
z
Principle point
Left-hand coordinate system. Uggh!
(but at least the math works out nicer…)

## Slide 3: Linear Pinhole Camera
(linear in homogeneous coordinates)
Projection model:
Light projects along straight line onto unit plane
To find the pixel index in each dimension,
multiply by pixels/unit (focal length)
add the index of the optic center

## Slide 4: Exercise
Using the information on the previous slides,
Suppose a camera has the following parameters:
Both focal lengths – 100 pixels/unit
Center – 50 pixels down, 75 pixels to the right
Find:
1. The i,j coordinates of the point (0,0,10)
2. The i,j coordinates of the point (0,10,10)
3. The i,j coordinates of the point (10,20,20)

## Slide 5: Prep for Lab Exercise
Given a pixel at [100, 400], find the location of the pixel on the unit plane.
  Also given: f = 100 pixels/unit (both directions), c = [200,300]
  (i comes first in all coordinates given here)
Given a pixel at [100, 345], find the location of the pixel on the unit plane.
  Also given: fi = 100 pixels/unit, fj = 90 pixels/unit, c = [200,300]
  (i comes first in all coordinates given here)

## Slide 6: Full calibration of a camera
Exercise: How many numbers are needed to calibrate this camera?