## Slide 1: CS-498 Computer Vision
Week 7, Day 1
  3D Camera Geometry (continued)
Notes: Print

## Slide 2: Pinhole Camera coordinate System
Optic center, t
Optic axis intersects unit plane perpendicularly
x
y
z
Principle point, c
Right-hand coordinate system forces z backwards…
Notes: 17q2: Corrected after class: Optic center shows up as a translation in equations, not as c.
Principle Point shows up as c in equations.

## Slide 3: Projection
[Draw 2-D projection here]
Notes: 17q2:Added after class

## Slide 4: Left or right-handed coordinate system?
Left Handed
Used by
  DirectX (Microsoft)
  POV-Ray (Pixar?)
  RenderMan (Pixar)
  VRML
  Glide
i = x/z
j = y/z
Right Handed
Used by
  OpenGL (e.g., NVIDIA)
  Physicists (simulation)
  The cross-product (?)
i = -x/z
j = -y/z
http://softwareengineering.stackexchange.com/questions/17519/why-does-directx-use-a-left-handed-coordinate-system#
Notes: 17q2:Added after class

## Slide 5: Linear Pinhole Camera
(linear in homogeneous coordinates)
Projection model:
Light projects along straight line onto unit plane
To find the pixel index in each dimension,
multiply by pixels/unit (focal length)
add the index of the optic center

## Slide 6: Exercise: Unit (or “unitless”) camera
Consider the equation
Substitute , ,
To get

## Slide 7: Exercise:
Re-write
In matrix form. Use [x;y;z;1] as the vector on the right-hand side of the equation.

## Slide 8: Intrinsic Calibration
The Intrinsic Parameters describe the part of the calibration that does not change if you move or rotate the camera
“Unit” camera:

## Slide 9: Conversion from unitless to pixel coordinates
fi = focal length in the i direction (pixels per unit distance along unit plane in the i direction)
fj = focal length in the j direction (pixels per unit distance along unit plane in the j direction)
ci = center of the image, measured in pixels
cj = center of the image, measured in pixels

## Slide 10: To find intrinsic calibration with pixel coordinates:

## Slide 11: “Full” camera
fi = focal length in the i direction (pixels per unit distance along unit plane in the i direction)
fj = focal length in the j direction (pixels per unit distance along unit plane in the j direction)
ci = center of the image, measured in pixels
cj = center of the image, measured in pixels
Because we chose right -handed coordinate system
And use i,j
instead of x,y

## Slide 12: Exercise
Using the information on the previous slides,
Suppose a camera has the following parameters:
Both focal lengths – 100 pixels/unit
Center – 50 pixels down, 75 pixels to the right
Find:
1. The ipix,jpix coordinates of the point (0,0,10)
2. The ipix,jpix coordinates of the point (0,10,10)

## Slide 13: Prep for Lab Exercise
Given a pixel at [100, 400], find the location of the pixel on the unit plane ()
  Also given: f = 100 pixels/unit (both directions), c = [200,300]
  (i comes first in all coordinates given here)
Given a pixel at [100, 345], find the location of the pixel on the unit plane.
  Also given: fi = 100 pixels/unit, fj = 90 pixels/unit, c = [200,300]
  (i comes first in all coordinates given here)

## Slide 14: Lab Exercise
Given i, j, and z… find x and y
Given a pixel at [100pix, 400pix]
  Also given: f = 100 pixels/unit (both directions), c = [200,300]
  Also given: The depth of the point () is 50 cm
Find the position of the point (x,y,z) in 3D space.
Include units.

## Slide 15: Extrinsic Calibration – Camera not at origin
Principal Point
Optic axis intersects unit plane perpendicularly
x
y
z
Axes may not be aligned with camera’s.
Origin may not be optic center
Optic
Center
Notes: 17q2: Corrected after class:
Principal Point is image center, optical center is different
Origin of x,y,z system moved and text clarified

## Slide 16: Full 6-DOF transform
Notes: 17q2: Text edited after class to reflect in-class discussion

## Slide 17: Full calibration of a camera
Exercise: How many numbers are needed to calibrate this camera?
Because we chose right -handed coordinate system
Notes: Edited after class to use the right-handed coordinate system we are using this quarter.

## Slide 18: Stopped Here Winter 2016-2017

## Slide 19: Extrinsics Parameters
What changes as the camera moves
Translation – position of optic center
  [x,y,z] – 3 numbers
Rotation – Multiplication of three rotation matrices, around each axis
  Roll, pitch, yaw – 3 numbers
  Matrix has 9 numbers, but these can
  be found from just 3, and will always have values
  between -1 and 1; very constrained.

## Slide 20: Radial Distortion
If we took a picture of concentric circles…
It might come out like…
This is radial distortion

## Slide 21: Radial Distortion Pinhole Camera
Projection model:
Light projects along straight line onto unit plane
Within unit plane, account for radial distortion
To find the pixel index in each dimension,
multiply by pixels/unit (focal length)
add the index of the optic center

## Slide 22: Equations for radial distotion
inew = iold (1+cx1iold2+cx2iold4+…)
jnew = jold (1+cy1jold2+cy2jold4+…)
This is a vector function:
(Both old and new are unit rather than pixel coordinates)

## Slide 23: Radial Distortion Intrinsics
Exercise: How many numbers are needed to calibrate this camera?

## Slide 24: Extrinsic Calibration – Camera not at origin
Principal Point
Optic axis intersects unit plane perpendicularly
x
y
z
Axes may not be aligned with camera’s.
Origin may not be optic center
Optic
Center
Notes: 17q2: Corrected after class:
Principal Point is image center, optical center is different
Origin of x,y,z system moved and text clarified

## Slide 25: Full calibration of a camera with radial distortion
Exercise: How many numbers are needed to calibrate this camera?
? --- Radial distortion magic here

## Slide 26: Homography as a “picture of a picture”
Suppose we take a picture of a picture with a pinhole camera that does not use radial distortion.
The original picture is on a plane, and we can represent points on that plane as