## Slide 1: SE3910 Week 3, Class 1
Circuits Exercises
Pulse-width modulation
Networking in Linux with C
Notes: Full agenda:
  Return Exam
  Questions about lab due tomorrow in class?
Threads: Locking on null object
Threads: invokeLater
Threads: The squares example
Decorator Class Diagram
More on Java IO
  Class diagrams
Design Principles
  in the patterns we’ve seen so far
Compare with alternatives
  Decorator vs. array approach suggested in class
    Non-decorator array – decorator can be added on without modifying the original hierarchy
    Decorator has “before-after” and possibly other combinatorial control that would be hard-coded in array
    [Show “screenshot” of discussion from class? Or just re-type?]
  Strategy vs. Decorator class diagrams side-by-side
  Structural difference (inheritance optional in Strategy pattern?)
  Decorator vs. “Strategy” array
Perhaps next:
Coding Starbuzz coffee (?)
Add real patterns
  ArrayList – null-checking
  Java I/O: Students do coding examples
  http://stackoverflow.com/questions/9358821/should-i-extend-arraylist-to-add-attributes-that-isnt-null

## Slide 2: Ex: What is the resistance of this resistor?
Notes: And what is the tolerance?

## Slide 3: Ex: GPIO safety
GPIO pins:
Sourcing limit: 4mA (current flowing out of BB)
Sinking limit: 8mA (current flowing in to BB)
Voltage: 3.3 V
Considering the resistor on the previous slide, is it large enough to not damage a GPIO pin configured as output, if the resistor ties the output to ground?

## Slide 4: Ex: This circuit is an attempt to wire a GPIO pin as both an input and an output
What happens if GPIO is an output with a value 1 and we press the switch?

## Slide 5: Some Technical Goals
How does one control the speed of a motor?
How does one change the brightness of a light-bulb?

## Slide 6: Pulse-Width-Modulation … in traffic

## Slide 7: Pulse-width modulation terminology
Determine the duty cycle (D)
Multiply the duty cycle by the peak voltage (Vp)

## Slide 8: In-class exercise
How can you control the brightness of an LED, using tools we have discussed so far?
How would you accomplish this if you went into lab right now?

## Slide 9: Advantages of Pulse-Width Modulation
Click to add text

## Slide 10: Sockets
A socket is defined as an endpoint for communication
Concatenation of IP address, port
  Transport-level Protocol: (e.g. TCP or UDP)
  Port 1625
  Host IP address:161.25.19.8
  Socket 161.25.19.8:1625
TCP also uses client’s IP and port to distinguish sockets
Communication consists between a pair of sockets
Notes: Draw picture as in slides

## Slide 11: Well-Known Ports
0 – 1023 Well known ports
7 Echo
20 ftp
22 ssh
25 smtp
37 time
70 gopher
79 finger
80 http
666 doom
992 telnet
1024 Registered Ports
1234 Mercurial / git
1309 Altera Quartus
1417 – 1420 Timbuktu Service
1500 IBM Tivoli
1534 Eclipse Agent Discovery
Etc

## Slide 12: Port and Address in POSIX C
in_port_t
  An unsigned integral type of exactly 16 bits.
in_addr_t
  An unsigned integral type of exactly 32 bits.
These are defined in systypes.h, I think
struct in_addr
{
n_addr_t s_addr;
}
istruct sockaddr_in
{ short sin_family; /* must be AF_INET */ u_short sin_port; struct in_addr sin_addr; char sin_zero[8]; /* Not used, must be zero */
};

## Slide 13
The socket() system call creates a new socket.
  3 arguments
    Address domain of the socket.
      AF_UNIX or AF_INET
    Type of socket.
      SOCK_STREAM or SOCK_DGRAM.
    Protocol.
      Usually 0

## Slide 14: Binding to a socket
bind() system call binds a socket to an address
Takes three arguments
  socket file descriptor
  address to which is bound
  size of the address to which it is bound
Just like in Java, only servers need to do this

## Slide 15: Listen & Accept
listen()
  Allows the process to listen for connections to a given socket
  Two arguments
    Socket file descriptor
    Number of queues that can be waiting
accept()
  Blocks until a client connects to a server

## Slide 16: Connect
Client side
  connect()
    int socket – file descriptor for the socket
    const struct sockaddr *address – the address to connect to
    socklen_t address_len – len of address
    returns 0 upon successful completion

## Slide 17: Read & Write
read() attempts to read nbyte bytes of data from the object referenced by the descriptor fd into the buffer pointed to by buf.
write()
  Writes data to the buffer

## Slide 18: See example code
server.c
client.c

## Slide 19: References
http://pubs.opengroup.org/onlinepubs/007908799/xns/syssocket.h.html
  syssocket.h
http://pubs.opengroup.org/onlinepubs/007908799/xsh/unistd.h.html
  unistd.h
http://pubs.opengroup.org/onlinepubs/7908799/xsh/systypes.h.html
  systypes.h – for xxxx_t

## Slide 20: I was asked this question in an interview today….
"When we create a thread with pthread_create() (POSIX Threads), the thread starts on its own. Why do we need to explicitly call start() in Java. What is the reason that Java doesnt start the thread when we create an instance of it."
I was blank and interviewer was short of time and eventually he couldnt explain the reason to me.
http://stackoverflow.com/questions/5269535/java-threads-vs-pthreads

## Slide 21: Threading
Java | Pthreads
java.lang.Thread | #include <pthread.h>
No external jar needed | link with -pthread
Thread t = new Thread(r) t.start(); | pthread_create(t,r,sr,a)
interface Runnable { void run(); } | Parameter: void* (*sr) (void *)
t.join(); | pthread_join(*t, &p)
Object o; | pthread_mutex_init(m,null)
synchronized(o) { … } … /* Garbage coll. */ | pthread_mutex_lock() … pthread_mutex_destroy()

## Slide 22: From Taylor’s
We can declare a function pointer by:
  uint8_t (*min)(uint8_t, uint8_t);
We can assign a function pointer to point to an actual function by:
  uint8_t minimum(uint8_t num1, uint8_t num2) {
  return num1 < num2 ? num1 : num2;
  }
  min = &minimum;
We can use it to call minimum using either of the following ways:
  uint8_t answer = min(3, 8);
  uint8_t answer = (*min)(3, 8);

## Slide 23: Threading
Java | pthreads
Object o; o.notify(); | phread_cond_t c = PTHREAD_COND_INITIALIZER; pthread_cond_broadcast(c);
o.wait(); | pthread_cond_wait(c,m);
o.notify(); | phtread_cond_broadcast(c);
Caveat: See http://wimhesselink.nl/pub/whh241b.pdf

## Slide 24: Possibly Fun
Very simple C++ wrapper for pthreads
  http://www.cs.utexas.edu/users/lavender/courses/cs345/lectures/CS345-Lecture-09.pdf
notify/wait – example comparison with Java and pthreads
  http://wimhesselink.nl/pub/whh241b.pdf
Compares create for Java, pthreads, and Win32 threads
  http://cs.millersville.edu/~csweb/lib/userfiles/9ThreadsII.pdf

## Slide 25: Certainly fun (Dr. Taylor’s Reviews)
http://msoe.us/taylor/tutorial/ce2810/functionpointers
  Function Pointers
http://msoe.us/taylor/tutorial/ce2810/csimilar
  C/C++/Java
http://msoe.us/taylor/tutorial/ce2810/ooc
  Object-Oriented C

## Slide 26: Other references
http://granite.sru.edu/~whit/cpsc464/Notes/figs/02-14.jpg
  Simple pthread chart
    From http://granite.sru.edu/~whit/cpsc464/Notes/ch2.html
https://pic.dhe.ibm.com/infocenter/iseries/v7r1m0/index.jsp?topic=%2Fapis%2Fusers_75.htm
  IBM example of using pthread_cond_init

## Slide 27: Standards
http://pubs.opengroup.org/onlinepubs/7908799/xsh/pthread.h.html
  pthead.h
http://pubs.opengroup.org/onlinepubs/7908799/xsh/systypes.h.html
  systypes.h – for xxxx_t

## Slide 28: References
EB: Derek Malloy, Exploring Beaglebone, Wiley, 2015