## Slide 1: SE3910 Week 4, Class 3
Notes on Lab 5
  Code to write!
Next week Monday
  Afternoon OH (after class) cancelled
  Ask questions before class if possible
Week 5, Wednesday
  Half-Exam 1
    Bring calculator!!!
    You may make a note-sheet for yourself
Notes: Full agenda:
  Return Exam
  Questions about lab due tomorrow in class?
Threads: Locking on null object
Threads: invokeLater
Threads: The squares example
Decorator Class Diagram
More on Java IO
  Class diagrams
Design Principles
  in the patterns we’ve seen so far
Compare with alternatives
  Decorator vs. array approach suggested in class
    Non-decorator array – decorator can be added on without modifying the original hierarchy
    Decorator has “before-after” and possibly other combinatorial control that would be hard-coded in array
    [Show “screenshot” of discussion from class? Or just re-type?]
  Strategy vs. Decorator class diagrams side-by-side
  Structural difference (inheritance optional in Strategy pattern?)
  Decorator vs. “Strategy” array
Perhaps next:
Coding Starbuzz coffee (?)
Add real patterns
  ArrayList – null-checking
  Java I/O: Students do coding examples
  http://stackoverflow.com/questions/9358821/should-i-extend-arraylist-to-add-attributes-that-isnt-null

## Slide 2: Notes on Lab
You can start on Lab 5:
  Install on the Beaglebone:
    the gpicview image viewer program and the OpenCV development libraries
    Compile boneCV.cpp on the BeagleBone
    Install the header files for compiling on the virtual machine
    Write, compile & review your code for the lab

## Slide 3: Places on campus with Wired internet connections
Some parts of CC third floor (the Mage corner)
Perhaps some rooms ground CC
Some SDL cubicles
Dorms – except for SMTP
Science building S365
Apartment (off-campus)

## Slide 4: Transmitting data
Physical Layer
  You didn’t talk too much about this in Network Protocols
  Can occur through many mediums
    Twisted Pair
    Coaxial Cable
    Fiber Optics
    Wireless

## Slide 5: Physical cable data rates
Sources: Dr. Schilling’s Slides and
http://en.wikipedia.org/wiki/Fiber-optic_communication
Wiring Type | Analog Bandwidth | 
CAT 3 | 16MHz | 
CAT 5 | 100 MHz | 
Coaxial Cable (50 Ohm) | 1-2 GHz | 
Fiber Optic Fiber (Single fiber) | 100 Tbit/s | 
Notes: Compare result with this
We got this far – working examples either again or for the first time and discussing new material.

## Slide 6: The Stroboscopic Effect
Have you ever noticed something that is in motion seem to stop?

## Slide 7: The Stroboscopic Effect (Aliasing)
http://upload.wikimedia.org/wikipedia/commons/7/77/Propeller_strobe.ogv
http://upload.wikimedia.org/wikipedia/commons/e/ef/The_wagon-wheel_effect.ogv

## Slide 8: Safety
See, e.g. http://www.seasshops.ucla.edu/services/student-faculty-shop/machine-shop-rules

## Slide 9: Aliasing
http://photo.stackexchange.com/questions/24512/what-is-aliasing-and-anti-aliasing

## Slide 10: More aliasing
Single-Sensor Imaging: Methods and Applications for Digital Cameras, by Rastislav Lukac
http://www.openphotographyforums.com/forums/showthread.php?t=14988

## Slide 11: Claude Shannon
H – analog Bandwidth
S – Signal power
N – Noise power

## Slide 12: Encoding audio signals digitally
How much data do we need to encode an audio signal?
[Matlab demo]
fsample > 2fmax audio frequency

## Slide 13: Sampling Theorem (again Nyquist)
fs = 2fm (fm is maximum frequency of signal)
Notes: Did not get to this.

## Slide 14: Buffering
With 1 KB buffer and 16-bit samples, there will be ____ samples per buffer
What is the maximum frequency analog singal that can be encoded, if the buffer holds 1 second of sound?

## Slide 15: Physical transmission: Latency vs. Bandwidth
Latency – delay to go over line
Bandwidth – rate of data
Can have high latency, high bandwidth (e.g. 1TB thumb-drive sneaker-net)
Can have low latency, low bandwidth (e.g. morse code through dedicated line)
[See MATLAB example]

## Slide 16: Noise, Latency, and Bandwidth
If we add noise to the line
  If the “noise” is other users sending packets
    Must resend whole packet – increases latency
    Transport-level
  If the “noise” is “white noise”
    Must use more redundancy – e.g. use more time per bit
    Decreases bandwidth, but latency is the same
    Link-level

## Slide 17: Signals as sums of sine-waves
[See Matlab demo]
http://mathworld.wolfram.com/FourierSeriesSquareWave.html
http://ccn.ucla.edu/BMCweb/SharedCode/slides/SlideFiles.html

## Slide 18: What is analog bandwidth?
Time
Freq.
http://www.mathworks.com/matlabcentral/fileexchange/22214-voice-audio-processing
Notes: Can do this not only with audio, but also with radio waves
Indeed, both are squared:
http://en.wikipedia.org/wiki/Parseval's_theorem

## Slide 19
Notes: For Digital TV:
http://transition.fcc.gov/mb/engineering/dtvmaps/
Full US allocations:
http://upload.wikimedia.org/wikipedia/commons/4/45/United_States_Frequency_Allocations_Chart_2003_-_The_Radio_Spectrum.jpg
VHF Usage (World wide)
http://upload.wikimedia.org/wikipedia/en/c/cc/VHF_Usage.svg

## Slide 20: Channel capacity

## Slide 21: In-class exercise
The old analog TV channels had a bandwidth of 6MHz
Supposing a SNR of 50 dB, what is the maximum possible bit-rate?
Notes: For Spring 2015 (15q3):
Work through one, then give an in-class exercise for the following.

## Slide 22: In-class Activity: What is the data rate of classic NTSC television (as digital stream)?
Store color with special scheme so only two bytes required per pixel, on average
720x480
30/1.001 fps
Follow up:
If compressed to 25MiB/s (or 25MB/s) what is the compression ratio?
Notes: [Draw out example on board]

## Slide 23: Human eye
Recall
  As little as 13ms
Notice interruption
  As short as 16ms
Single-ms duration looks as long as
  100-400ms
10ms green followed by 10ms red
  May appear as single yellow stimulus

## Slide 24: Ex:
Why might you want to sample at a higher frame-rate than the 30fps?
Be as professional as possible
  Avoid flame wars
  Have technical depth to back it
  Avoid sounding technical just to be cool

## Slide 25: Ex:
What are two ways we can avoid the stroboscopic effect in a video game simulation of a rotating wheel?

## Slide 26: In-class Activity: Analog to digital bandwidth
Suppose you would like to send video in a (relatively) low-frequency with a narrow bandwidth of 1 Mhz
The connection is fairly noisy and you can only get 20dB SNR
What bit-rate can you achieve?
Why have manufacturers re-defined MB, etc?
Notes: http://www.arrl.org/files/file/Regulatory/Recommended_Practices_Version_6_5.pdf
Earlier draft:
Modern Digital TV uses the same channels as analog TV, but dynamically maps them.
But each channel is now re-used by allocating virtual “sub-channels” within the main channel that use less of the bandwidth.
This is done digitally
[And as a result, the channel width is about the same]

## Slide 27: In-class activity
Suppose I have a band centered at 100 Mhz which is 1Mhz wide.
What are the limits on this range?
What is the wavelength of the center 1 Mhz signal
speed of light = 299 792 458 m / s
speed in Cat-5 is 70% of this
wavelength = time of period * velocity
Notes: http://www.eham.net/ehamforum/smf/index.php?topic=56160.0

## Slide 28: Fiber-optic Transmission
In fiber-optic transmission, signals are sent by transmitting various colors (or invisible) light down a fiber-optic channel
The colors are separated at the other end
Multiple fibers can be used
Supposing that the same bandwidth rule applies, what bandwidth can be carried by the visible spectrum? (700-400nm)
Use SNR of 4000
Hint: Convert wavelength to period/frequency
Notes: http://physics.stackexchange.com/questions/56240/maximum-theoretical-bandwidth-of-fibre-optics
So, let's begin by exploring the best way to use our power. If we devote it to M symbols per second, each of our measurements comprise the detection of N=PMhν0 photons, thus our signal to noise ratio is SNR=NN√=PMhν0−−−−−√. By the Shannon-Hartley form of the Noisy channel coding theorem(see also here), we can therefore code our channel to get log2(1+PMhν0−−−−−√) bits of information per symbol, i.e. Mlog2(1+PMhν0−−−−−√) bits per second through our optical fibre. This is a monotonically rising function of M, so a limit on P by itself does not limit the capacity.
However, by a converse of the Nyquist-Shannon sampling theorem we can send a maximum of Bsymbols down the channel per second. This then is our greatest possible symbol rate. Hence, our overall expression for the fibre capacity in bits is:
C=Blog2(1+PBhν0−−−−−√) bits per second

## Slide 29: References
EB: Derek Malloy, Exploring Beaglebone, Wiley, 2015