## Slide 1: CMOS Logic Gates

## Slide 2: NMOS transistor acts as a switch
When gate voltage is 0 V
  No channel is formed
  current does not flow easily
  “open switch”
When gate voltage is above threshold voltage
  electrons are drawn into channel
  current can flow through channel with little resistance
  “closed switch”
MOS transistors can be used as a voltage-controlled switch
This is the basis of computing with 1’s and 0’s!

## Slide 3: Simplified Transistor Model
Simple model for transistors in CMOS circuits, when VIN is fully logic 0 or logic 1:
D
G
S
VGS = 0 V
VGS = 5V (for NMOS)
VGS = -5V (for PMOS)
D
G
S
Transistor is cutoff.
Zero current flow.
Transistor is not cutoff, but zero current flow of partner transistor causes VDS = 0 V.

## Slide 4: Logic Gates
We may cleverly position the transistors so that when a combination of high and low voltages is applied at the input, an output voltage appears according to a useful logic function.
We call such a circuit a logic gate.
We express the operation of the logic gate using a truth table that shows the output (high or low) for each possible combination of high and low input voltages.

## Slide 5: Inverter (NOT Gate)
D
S
VDD
D
S
VOUT
VIN
Functional Representation
(Symbol)
Physical Representation
(CMOS circuit)
How much detail do you need to show for your application?

## Slide 6: Inverter (NOT Gate)
Functional Representation
(Symbol)
A | NOT A A
0 | 1
1 | 0
Truth Table
A
NOT A

## Slide 7: Verify CMOS Inverter (use switch model)
D
S
5 V
D
S
VOUT
VIN
0 V

## Slide 8: Verify CMOS Inverter (use switch model)
D
S
5 V
D
S
VOUT
VIN
5 V

## Slide 9: AND Gate
Functional Representation
(Symbol)
A B | A AND B A·B
0 0 | 0
0 1 | 0
1 0 | 0
1 1 | 1
Truth Table
A
B
A AND B

## Slide 10: NAND Gate
Functional Representation
(Symbol)
A B | A NAND B A·B
0 0 | 1
0 1 | 1
1 0 | 1
1 1 | 0
Truth Table
A
B
A NAND B

## Slide 11: CMOS NAND
5V
A
B
S
S
S
S
AB

## Slide 12: More Practice
Verify the logical operation of the CMOS NAND:
A
= 0V
B
= 0V
A
= 0V
B
= 5V
5V
S
S
S
S
5V
S
S
S
S

## Slide 13: More Practice
Verify the logical operation of the CMOS NAND:
A
= 5V
B
= 0V
A
= 5V
B
= 5V
5V
S
S
S
S
5V
S
S
S
S

## Slide 14: OR Gate
Functional Representation
(Symbol)
A B | A OR B A+B
0 0 | 0
0 1 | 1
1 0 | 1
1 1 | 1
Truth Table
A
B
A OR B

## Slide 15: NOR Gate
Functional Representation
(Symbol)
A B | A NOR B A+B
0 0 | 1
0 1 | 0
1 0 | 0
1 1 | 0
Truth Table
A NOR B
A
B

## Slide 16: More Practice
Verify the logical operation of the CMOS NOR:
A
= 0V
B
= 0V
A
= 0V
B
= 5V
S
S
S
S
5V
S
S
S
S
5V

## Slide 17: More Practice
Verify the logical operation of the CMOS NOR:
A
= 5V
B
= 0V
A
= 5V
B
= 5V
S
S
S
S
5V
S
S
S
S
5V

## Slide 18: CMOS Networks
Notice that VOUT gets connected to either VDD or ground by “active” (not cutoff) transistors.
We say that these active transistors are “pulling up” or “pulling down” the output.
NMOS transistors = pull-down network
PMOS transistors = pull-up network
These networks had better be complementary or VOUT could be “floating”—or attached to both VDD and ground at the same time.

## Slide 19: CMOS NAND vs. NOR
CMOS NAND
5V
S
S
S
S
S
S
S
S
5V
CMOS NOR

## Slide 20: XOR and XNOR Gates
A B | A XOR B A ⃝ B
0 0 | 0
0 1 | 1
1 0 | 1
1 1 | 0
A XOR B
A
B
A B | A XNOR B A ⃝ B
0 0 | 1
0 1 | 0
1 0 | 0
1 1 | 1
A XNOR B
A
B
+
+