## Slide 1: SE3910 Week 1, Class 1
Today – Introductions
  The students (informally)
  The instructor
  Safety Review
  Policy
  The course
Tomorrow (If you are in that section)
  Lab 1, S365 (Purchase Beaglebone black kit BEFORE)
Wednesday
  Class 1-2, here (CC118)
Notes: Full agenda:
  Return Exam
  Questions about lab due tomorrow in class?
Threads: Locking on null object
Threads: invokeLater
Threads: The squares example
Decorator Class Diagram
More on Java IO
  Class diagrams
Design Principles
  in the patterns we’ve seen so far
Compare with alternatives
  Decorator vs. array approach suggested in class
    Non-decorator array – decorator can be added on without modifying the original hierarchy
    Decorator has “before-after” and possibly other combinatorial control that would be hard-coded in array
    [Show “screenshot” of discussion from class? Or just re-type?]
  Strategy vs. Decorator class diagrams side-by-side
  Structural difference (inheritance optional in Strategy pattern?)
  Decorator vs. “Strategy” array
Perhaps next:
Coding Starbuzz coffee (?)
Add real patterns
  ArrayList – null-checking
  Java I/O: Students do coding examples
  http://stackoverflow.com/questions/9358821/should-i-extend-arraylist-to-add-attributes-that-isnt-null

## Slide 2: Equipment
Purchase beaglebone black kit (~$65) from Tech Support
  Used in Lab 2
(Optional) Tools – e.g. needle-noise pliers
Check out short-term
  Kit (breakout board, breadboard cape, LCD cape, USB Oscilloscope)
  Small parts (also may desire to purchase)

## Slide 3: Course Overview
(See schedule, take notes)

## Slide 4: Flow Examples
For two minutes, write down with your team a list of as many things that flow that you can think of.

## Slide 5: What causes things to flow?
For a few examples, let’s think about WHY the flow occurs. What makes it flow faster or slower?

## Slide 6: What is Voltage?
Suppose I rub my shoes across the floor…
“Voltage” is what exists between my finger and the doorknob before I touch it.
Does voltage require current to exist?
Variable Name: V (Or, rarely, E (electromotive force))
Voltage is measured in Volts (V). We celebrated Alexandra Volta’s birthday a few weeks back.

## Slide 7: What is current?
Current is what exists when I touch the doorknob. It is the flow of charge
Does current require voltage to exist?
Variable name: I
Current is measured in Amps. (A) One amp is (for this course) a LOT of current!

## Slide 8: A Very Simple Circuit
What is the voltage across the resistor?
Power Supply
Resistor
+
+
-
-
5V

## Slide 9: Resistance
Measures how much a device keeps current from flowing through it. More resistance, less current flow. (all other things being equal)
The variable name is usually R
The units are Ohms (Ω)
  Ω = V/A
For the purposes of this class, 1Ω is very small.
  “Resistance is futile if < 1Ω” (Or even 10 Ω)

## Slide 10: Resistance
V=IR
For a given resistor,
  If current increases, voltage …
  If voltage increases, current …
For a given voltage,
  If the resistance increases, the current…

## Slide 11: Resistance
V=IR
Exercise: Suppose we have 3.3V across a 1 Ohm resistor. What is the current through the resistor?

## Slide 12: Power
Exercise: How do you compute energy in Physics?
What are the units for energy?
Exercise: How do you compute power in Physics (excluding electricity?) Write as many examples as you can.
What are the WI units for power?
How do you computer power in circuits?

## Slide 13: Power
Substituting in V=IR, we find…
Exercise: Find a formula without V.
Exercise: For a given resistor, if I double the voltage, how does the power change?
http://www.electronics-tutorials.ws/resistor/res_7.html
http://paperclip.rcs.ac.uk/index.php/Basic_Electrical_Theory

## Slide 14: Power
Suppose I have a 1Ω resistor with 3V across it.
  What is the current through the resistor?
  What is the power through the resistor?
  What do you think will happen if the resistor is a ¼ Watt resistor? (As many are)

## Slide 15: Cartoon
One source: http://www.sengpielaudio.com/calculator-ohmslaw.htm

## Slide 16: Review: Voltage & Current
What is the voltage across the resistor?
Power Supply
Resistor
+
+
-
-
5V

## Slide 17: Review: Resistance & Power
Exercise: According to this answer,
20mA is (possibly) enough to fibrillate
your heart. Supposing your internal
resistance is 100 Ω, what voltage is
needed?
Image sources: http://www.electronics-tutorials.ws/resistor/res_7.html
http://paperclip.rcs.ac.uk/index.php/Basic_Electrical_Theory
Notes: A

## Slide 18: Example 1: Open switch
Compute all currents & voltages

## Slide 19: Example 2: Closed switch
Compute all currents & voltages

## Slide 20: Example 3: Charging a battery
If 30mA desired through VL (charging), what should R be?

## Slide 21: Example 4: Powering an LED
If 30mA desired through L1 what should R be? (Voltage drop across L1 is 2 V, regardless of current)

## Slide 22: Exercise:
Illustrate two threads running in parallel on a sequence diagram.

## Slide 23: Parallel Resistors
Kirchoff’s Voltage Law
  Voltage is between points, regardless of path
Kirchoff’s Current Law
  Current splits
(Similarly)
Series Resistors

## Slide 24: Equivalent Resistance
Resistors that are wired in parallel or series behave exactly like their equivalent resistor
  If we know voltage, can find current
  If we know current, can find voltage.
It can be tricky to recognize parallel and series circuits

## Slide 25: Warning…
Originally from: http://www.thegooglestory.com/glat.html
http://xkcd.com/356/

## Slide 26: Examples
At which dot is the "pressure" (voltage) highest in each circuit? If time: Which circuit draws more current?

## Slide 27: Resistor Limits
A resistor follows Ohm’s law; V=IR
http://physics.stackexchange.com/questions/55534/physical-interpretation-of-y-intercept-in-a-current-vs-voltage-graph

## Slide 28: How do resistors fail?
They burn up, literally
For many resistors, the maximum steady-state generation of heat they can handle is ¼ watt
Can calculate with P = IV = V2/R = I2R (subbing in V=IR)
Ex: Find the minimum ¼ W resistance that is safe with a (non-Beaglebone) 3.3 V source?

## Slide 29: How do diodes fail?
Same way as resistors – they burn up
So total temperature is the limiting factor
If a voltage is applied across an LED current will flow through the LED
The higher the voltage, the more current will flow
But this does NOT follow Ohm’s Law; V≠IR
How to determine max V or I?

## Slide 30: LED current-voltage curves
http://www.ecse.rpi.edu/~schubert/Light-Emitting-Diodes-dot-org/chap04/chap04.htm

## Slide 31: Our “mental model(s)” for diodes
https://www.st-andrews.ac.uk/~www_pa/Scots_Guide/info/comp/passive/diode/chars/chars.htm

## Slide 32: LED current and voltage limits
So if we apply a voltage higher than the transition Vd to the LED (c), the current will be…
If we force a current in the 0.5 mA range through the LED (c), the voltage will be …
Ex: Decide will more likely damage the component? 1 mA or 2V? Explain.

## Slide 33: Selecting an LED resistance value
Suppose L1 is a diode with Vd = 1.8 V
Ex: Write a formula relating the current through L1 to R1.
Ex: Solve for R1 if we want the (max) current to be 10 mA.