## Slide 1: Polling vs. Interrupts
Notes: Interrupts: “Cut it out! I’ll tell you when we’re there!”

## Slide 2: SE3910 Week 2, Class 1
Today
  Real-Time Systems
Week 3 Lab
  Quiz 2
    More circuits?
    Real-time systems
    Latency
    …?
  Lab 3 – Measuring Latency
    Complete prelab before lab – GB downloads, etc.
Notes:   17q3: 1-4,8-15
Full agenda:
  Return Exam
  Questions about lab due tomorrow in class?
Threads: Locking on null object
Threads: invokeLater
Threads: The squares example
Decorator Class Diagram
More on Java IO
  Class diagrams
Design Principles
  in the patterns we’ve seen so far
Compare with alternatives
  Decorator vs. array approach suggested in class
    Non-decorator array – decorator can be added on without modifying the original hierarchy
    Decorator has “before-after” and possibly other combinatorial control that would be hard-coded in array
    [Show “screenshot” of discussion from class? Or just re-type?]
  Strategy vs. Decorator class diagrams side-by-side
  Structural difference (inheritance optional in Strategy pattern?)
  Decorator vs. “Strategy” array
Perhaps next:
Coding Starbuzz coffee (?)
Add real patterns
  ArrayList – null-checking
  Java I/O: Students do coding examples
  http://stackoverflow.com/questions/9358821/should-i-extend-arraylist-to-add-attributes-that-isnt-null

## Slide 3: What would you most like to do?
Please take this survey: (You only need to pick 5)
http://pollmill.com/f/what-would-you-most-like-to-do-m6e93hx.fullpage
– OR –
http://bit.ly/1F9RxRo
And then….
http://pollmill.com/private/forms/what-would-you-most-like-to-do-m6e93hx/answers

## Slide 4: Real-time and Embedded
Real-Time
  responding as rapidly as required by the user or the process being controlled.
  - Random House Dictionary (Abbrev.)
Embedded System
  A combination of hardware & software to perform a specific function
  -Dr. Schilling’s slides
  Often real-time
Notes: Real-Time System Examples:
Temperature control of a chemical reactor
Space mission control system
Nuclear power generator system
Many safety-critical systems
Click-drag in a GUI
Hospital reports delivered within minutes
Examples of Systems Containing Embedded Systems
Appliances: microwaves, VCRs, dishwashers, refrigerators, furnaces, clocks
Medical devices: hearing aids, pacemakers, …
Car systems: antilock brakes, engine timing and monitoring, seat/mirror positioner, air handling, lighting/environment
Mobile phones, PDA’s, Music players, remote controls
Diagram one of these devices, label the Real-time system and the Embedded Real-time system

## Slide 6: What is a system?
System
A mapping from a set of inputs to outputs

## Slide 7: Example: Weather Monitor
Notes: See summary Slide 1
Aka FBDs – Functional Block Diagrams
FIGURES 1-3
Draw on board:
LED sub-system
Inputs:
Wind direction (as 5v power supply to each LED)
Outputs:
Light in a pattern indicating the wind direction
ADC
Analog-to-Digital Converter
Inputs:
Wind direction from weather vane as voltage read (0- 5v)
off of a potentiometer (more on this)
Outputs:
Wind direction from weather vane as serial 5 volt stream.
(Figure)
NOT as USB serial stream
EXAMPLE
Microprocessor Scheduler Module
Input:
Tasks to be scheduled
(Data written to memory locations in the processor, Interrupts)
Output:
Sequenced scheduled tasks

## Slide 8: Response Time & Latency
Response Time
  The time between input events and all possible output events
Release Time
  When a process is ready to start

## Slide 9: Response Time & Latency
Latency - a time delay between stimulus and response, or between cause and effect (Wiki)
  Memory Latency – Delay between write & read (Wiki)
  Interrupt Latency – Delay between stimulus and starting handler
  Audio Latency – Delay from audio in to audio out of a system (=response time)
  Network Latency – Delay from send to receive [or …]
Conclusion: Latency = response time, possibly for a sub-system

## Slide 10: Real-Time System Terminology
Soft
  No system failure on failure to meet response time requirement (deadline)
Firm
  System failure on failure to meet multiple deadlines
Hard
  System failure on failure to meet a single deadline
Notes: This is a real-time systems definition

## Slide 11: Exercise
On your own: Write which kind of real-time system is being used
With your partner, discuss & fill in the explanations
System | Classification | Explanation
Video Surveillance System for Car Dealership |  | 
Laser welding robot to construct car frames |  | 
2 player air hockey game on game console |  | 

## Slide 12: Five Misconceptions (paraphrased from Laplante and Ovaske)
Real-time systems are fast
All you need is
  a real-time OS
  a rate-monotonic scheduler
  lots of scheduling theory
We’ve figured out how to make real-time systems
Notes: Draw graph illustrating Rate-monotonic
See hand notes

## Slide 13: Microcontroller vs. Microprocessor
Microprocessor
  a single chip holding a single (large) CPU
  what most PC’s have
Microcontroller
  A single chip holding a CPU, memory, peripherals
  What’s on the Beaglebone Black

## Slide 14: System on a Chip vs. MicroController
Microntroller – see previous
System on a Chip
  broader
  will include microcontroller
  may include more, for example
    analog components
    CE1901/CE1911 students use a SoC consisting of a microprocessor and an FPGA
Notes:   a bit of a buzzword – every manufacturer has their own meaning

## Slide 15: The AM 335x (The Beaglebone’s CPU chip)
http://www.ti.com/lit/ds/symlink/am3358.pdf
Notes: http://www.ti.com/lit/ds/symlink/am3358.pdf

## Slide 16: An i5 (Intel chip in laptop)
http://aphnetworks.com/reviews/intel_core_i5_750/2
Notes: What’s the difference? i5 really NEEDS external memory to work, the AM335x’s could, in theory operate without external memory
(And my first attempts to find something like the above found the “chipset” instead.)
This page:
http://www.bjorn3d.com/2010/01/intel-i5-661-3-33ghz-dual-core-cpu/
says that the i7 chip includes graphics (i.e. GPU). Wow!

## Slide 17: Timing Terminology
Event
  A jump in the program counter
Synchronous
  Predictable. Scheduled. In sync with other events
Asynchronous
  Unpredictable. Unscheduled. External requests
Aperiodic – No fixed period, asynchronous
Sporadic – Extremely infrequent and aperiodic
Punctual – Neither early nor late
Notes: Draw pictures of time sequence for synchronous and asynchronous events.
Do Comparison table

## Slide 18: What is an event?
for example, in SE 1021

## Slide 19: I/O hardware
Inside the device
External pin
Laplante and Ovaske 4E, p. 52
Notes: Custom text, p. 57
Laplante and Ovaske 4E, p. 52
Polling hardware is easy
Interrupts require some additional hardware
PIU – peripheral Interface Unit

## Slide 20: Interrupt Definitions
Interrupt
  An event in hardware that triggers the processor to jump from its current program counter to a specific point in the code.
Interrupt Service Routine (ISR)
  The function that is called or the particular assembly code that is executed when the interrupt happens is called the Interrupt Service Routine (ISR).
Interrupt flag (IFG)
  this is the bit that is set that triggers the interrupt, leaving the interrupt resets this flag to the normal state.
Interrupt Enable
  Control bit that tells the processor that a particular interrupt should or should not be ignored.
Interrupt Vector Table
  A table in memory which maps ISRs to interrupts.

## Slide 21: ISR Handling (1)
[Discussed at high level – Interrupt like any other event, only triggered by hardware]

## Slide 22: ISR Handling (2)
Fig 2.14 p. 54 Laplante and Ovaske 4E
PIU – Peripheral interface unit
Notes: Fig 2.14 p. 54 Laplante and Ovaske 4E
PIU – Peripheral interface unit
Acknowledgement not described in text, that I can see
Important point: Interrupt Vector is sent to CPU telling it which interrupt occurred.