## Slide 1: SE3910 Week 3, Class 2
Today
  Nervous System Response Time

## Slide 2: Measure your class-mate’s response time
SE3910 Week 3, Class 2

## Slide 3: Instructions
Part 1
  One partner should hold the stick while the other partner places their hand around the tape at the end of the stick. Hands should be approximately 1” from the stick.
  At some point in the future, the partner drops the stick. Read the numbers off of the stick for response time and record them in the GoogleDoc.
  Repeat the experiment 3 times
Part 2
  One partner should hold the stick while the other partner places their hands around the tape at the end of the stick. Hands should be approximately shoulder width apart.
  At some point in the future, the partner drops the stick. Read the numbers off of the stick for response time and record them in the GoogleDoc.
  Repeat the experiment 3 times
Partners swap roles…

## Slide 4: Human Systems
Sensory:
Inputs: Both external & internal
Outputs: Nerve signals
Nervous:
Inputs: Nerve signals
Outputs: Intelligent nerve signals
Motor:
Inputs: Nerve signals
Outputs: Precise & powerful motion

## Slide 5: Human Nervous System

## Slide 6: Nerve Speeds
Speed of signal transmission along nerve fibers
  depends on diameter of fiber & presence of myelin
  large fibers have more surface area for signals
Speeds
  small, unmyelinated fibers = 0.5 - 2.0 m/sec
  small, myelinated fibers = 3 - 15.0 m/sec
  large, myelinated fibers = up to 120 m/sec
Functions
  slow signals supply the stomach & dilate pupil
  fast signals supply skeletal muscles & transport sensory signals for vision & balance

## Slide 7: System Diagram
Delays
  Distance from stick to eyes
    Speed of light = 299 792 458 m / s (google)
  Neuron distance between eyes and brain stem
    .1 metre
  Neuron distance between brain and hands
    1 metre
  Time for hands to close
    Hands can move up to 100 mph (44 metres per second)
  Rest of time will be latency in the brain

## Slide 8: Exercise:
Compute the response time of the brain by subtracting all the remaining latency components from the measured latency of the stick capture.

## Slide 9: Some Technical Goals
How does one control the speed of a motor?
How does one change the brightness of a light-bulb?

## Slide 10: Pulse-Width-Modulation … in traffic

## Slide 11: Pulse-width modulation terminology
Determine the duty cycle (D)
Multiply the duty cycle by the peak voltage (Vp)

## Slide 12: In-class exercise
How can you control the brightness of an LED, using tools we have discussed so far?
How would you accomplish this if you went into lab right now?

## Slide 13: Advantages of Pulse-Width Modulation
Click to add text

## Slide 14: References
EB: Derek Malloy, Exploring Beaglebone, Wiley, 2015