## Slide 1: SE3910 Week 4, Class 1
Today
  Real-Time Operating Systems
  Scheduling
  Rate Monotonic Analysis
In Lab: Quiz
  More circuits? More resistors?
  More data-rate estimates
  Real-time Operating Systems
  Rate Monotonic Analysis
Notes: 17q3:
1-2,4,6-7,10-15,17,22,26-36
Print slides 20,21 on half sheets

## Slide 2: Course Learning Outcomes
Understand concepts of time-critical computing and identify real-time systems
Get familiar with a host-target development environment for time-critical systems
Write multitasking computer programs with inter-task communication and synchronization
Apply concepts of inter-task communication and synchronization via shared memory, message queues, signals, semaphores, mailboxes
Understand real-time kernels and task scheduling
Understand concepts of reliability in relation to real-time software
Construct distributed real-time applications using a commercial Real-Time Operating System
Analyze the performance of a real-time system
http://catalog.msoe.edu/preview_course_nopop.php?catoid=14&coid=15008&
Notes: Bold – coming up
Italics – already done
Red – coming up next

## Slide 3: Textbook references
This material comes from
  Chapter 4 of last year’s custom text
  Chapter 3 of Laplante & Ovaska, Real-Time Systems Design and Analysis, 4th ed.

## Slide 4: Real-Time Operating Systems
What is a hard real-time system?
What is a real-time operating system?

## Slide 5: Lab 3 Spring 2016 response times button-press to LED
Chart: 
Notes: Note the long tails – if this is a hard real-time system, it must have a deadline of …
1 ms?
2 ms?
4 ms?
6 ms?
10 ms?
100 ms?
What about if the network is involved?

## Slide 6: Exercise
Name as many OS components (non-essential or essential) as you can

## Slide 7: Exercise
Organize the classes’ components from the previous slide into non-essential, maybe, and essential

## Slide 8: Levels of Operating Systems

## Slide 9: Scheduling Theory
What is a schedule?

## Slide 10: Round-Robin Scheduling
Round-Robin with Timed Interrupts

## Slide 11: Round-Robin Scheduling with pre-emption
Round-Robin with Synchronous & Asynchronous Interrupts

## Slide 12: Cyclic Code Scheduling
Scheduling decisions are made periodically rather than arbitrarily
  Major cycle (hyperperiod)
    The minimum time required to execute tasks allocated to the CPU
    Equal to the least common multiple of the task periods
  Frames
    The locations where scheduling decisions are made
    No pre-emption within frames
Notes: p.100-101
Illustrate these definitions.

## Slide 13: Optimal Cyclic Code Scheduling – Rate Monotonic Scheduling
Notes: Write out by hand
- use creative spacing to emphasize structure

## Slide 14: Predicting CPU usage
τi – task i
pi – period i (ms)
ei – execution time (ms)
ui -- %CPU used for task i

## Slide 15: Predicting CPU usage (2)
ui = ei/pi
U =

## Slide 16: In-Class Exercise
Calculation: What is the processor utilization for this problem?
Based on RMA, what order will they execute and how will they execute?
Hints: Draw release times, break up processing into multiple frames if needed.
Notes: Skip calculation if time short

## Slide 17: Rate-Monotonic Example
Notes: See example soln. in text.

## Slide 18: Predicting CPU usage
τi – task i
pi – period i (ms)
ei – execution time (ms)
ui -- %CPU used for task i
Task | priority (1 highest) | ei (ms) execution time | pi (ms) period | ui (%) CPU time
t1 |  | 2 | 6 | 
t2 |  | 4 | 9 | 
t3 |  | 3 | 18 | 

## Slide 19: Predicting CPU usage (2)
ui = ei/pi
U =

## Slide 20: In-Class Exercise
Calculation: What is the processor utilization for this problem?
Based on RMA, what order will they execute and how will they execute?
Hints: Draw release times, allow interruptions at frame boundaries if needed.
Task | priority (1 highest) | ei (ms) execution time | pi (ms) period | ui (%) CPU time
t1 |  | 2 | 6 | 
t2 |  | 4 | 9 | 
t3 |  | 3 | 18 | 
Notes: Skip calculation if time short

## Slide 21: Rate-Monotonic Example
1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Task number
Task | priority (1 highest) | ei (ms) execution time | pi (ms) period | ui (%) CPU time
t1 |  | 2 | 6 | 
t2 |  | 4 | 9 | 
t3 |  | 3 | 18 | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | ms
Notes: See example soln. in text.

## Slide 22: Simplifying Assumptions needed for RMS
All tasks in the task set considered are strictly periodic – release times happen exactly on the period
The relative deadline of a task is equal to its period – deadline is on next period
All tasks are independent; there are no precedence constraints.
No task has any nonpreemptible section, and the cost of preemption is negligible.
Only processing requirements are signiﬁcant; memory and I/O requirements are negligible.

## Slide 23: Scheduling Definitions
Notes: Define d_i,j as well
Skip laxity if desired.

## Slide 24: (cont.)
Notes: Illustrate the definitions rather than using words.
Third line: Assuming deadline = period (assumption made on next slide)

## Slide 25: More on the Rate Monotonic Analysis
Why is it called Rate Monotonic?
When is RMA guaranteed to work?

## Slide 26: Why is it called Rate Monotonic?
What do you think of when you hear the word monotonic?

## Slide 27: When is Rate Monotonic Guaranteed to work?
For n tasks, RMA is guaranteed to meet all deadlines if
For a very large number of tasks (n approaching infinity), RMA is guaranteed to meet all deadlines if
For many practical applications, RMA will work if (See Lehoczky et. al 1989)
Notes: Their assumption is that the task periods are uniformly distributed in the range [1 B], where if B>50, U<=.85 is guaranteed(?) to meet the deadline on average…

## Slide 28: Building your own micro-kernel
You may choose to run really light-weight because
You want the system to be more predictable
To minimize overhead
In this case, you can write your own super-simple OS or micro-kernel. Here are a few varieties

## Slide 29: Micro-kernel: Simple polled loop
int main(int argc, char **argv) {
while(true) {
if(packet_here) {
process_data();
packet_here = 0;
}
}
}

## Slide 30: Micro-kernel: Polled loop with delay
int main(int argc, char **argv) {
while(true) {
if(packet_here) {
process_data();
pause(21); // ms
packet_here = 0;
}
}
}

## Slide 31: Micro-kernel: Cyclic code structure
int main(int argc, char **argv) {
while(true) {
task1();
task2();
task3();
}
}
(Not to be confused with Cyclic Code Scheduling)

## Slide 32: Micro-kernel: Cyclic code structure with high-rate task 2
int main(int argc, char **argv) {
while(true) {
task1();
task2();
task3();
task2();
}
}

## Slide 33: Micro-kernel: Co-routines
void task1() { // called from a cyclic loop like
// previous slide
if(state == state1) {
phase1_1();
} else if(state == state2) {
phase1_2();
} else if(state == state3) {
phase1_3();
}
}
/* task 2 is similar... */
This implements a state machine.
Co-routines require a great deal of discipline to write correctly. Ada has constructs to help…

## Slide 34: Micro-kernel: Interrupt-driven
int main(int argc, char **argv) {
while(true) {/* idle loop */}
}
void int1() {
saveContext();
work1();
restoreContext();
}
void int2() {
saveContext();
work2();
restoreContext();
}
void int3() {
saveContext();
work3();
restoreContext();
}

## Slide 35: What to do if a second interrupt occurs?
Disable interrupts
Interrupt the interrupt… "Preemptive priority"

## Slide 36: Micro-kernel: Foreground-background System
int main(int argc, char **argv) {
while(true) {
do_low_priority();
}
}
void int1() {
saveContext();
work1();
restoreContext();
}
void int2() {
saveContext();
work2();
restoreContext();
}
void int3() {
saveContext();
work3();
restoreContext();
}

## Slide 37: Foreground-background systems
Note this is the most general type of system. Depending on what code we use for do_low_priority() and for the int1(), int2(), etc methods, we can implement any of the other systems, even the co-routines one.
(For those without interrupts, there aren't interrupt routines)
(For the pure interrupt approach, we use an empty method for do_low_priority())

## Slide 38: References
EB: Derek Malloy, Exploring Beaglebone, Wiley, 2015
Laplante and Ovaska, Real-Time Systems Design and Analysis, Fourth Edition, Wiley, 2012
Lehoczky, Sha, and Ding “The rate monotonic scheduling algorithm: exact characterization and average case behavior” Proceedings of the Real Time Systems Symposium, 1989